## Slide 1: IoT & Puck.js Training Course
Tee Ting Yi | NTU | May 2017

## Slide 2
Interconnection (‘Internet’) between embedded devices with communication abilities (‘Things’)
Integration of physical world into virtual world
  e.g.: Receive physical environment data from sensor in IoT and send data to computer system
Convergence of multiple technologies: Ubiquitous wireless connection, real-time analytics, machine learning, commodity sensors, embedded systems
IoT Introduction

## Slide 3
IoT Trend

## Slide 4
Connectivity: Able to communicate with another device, preferably using Bluetooth 5 with improved connectivity
Heterogeneity: Able to interact with other devices or service platforms through different network
Durability: Able to withstand physical environment conditions and long battery life
Physical safety: Hard to tamper device / damage users
Easy to program and deploy
IoT Controller: Characteristics

## Slide 5
Designed for IoT
Low energy (LE) – reduce power consumption
Uses mesh network topology – making IoT scalable, no need to worry about range of Bluetooth
Bluetooth 5

## Slide 6
Up to 2x bandwidth with low energy
  From 1Mbps to 2Mbps
Up to 4x range with low energy
  From ~80m to ~200m
Up to 8x broadcasting message capacity
  From 31 bytes to 255 bytes
Interoperability improvement: communication between compatible profiles
Backwards compatible
Bluetooth 5 VS Bluetooth 4.2

## Slide 7: What is Puck.JS?
A programmable “button”
Contains many sensors, LEDs and GPIO pins
Supports Physical Web, Web Bluetooth, NFC,
Bluetooth 5 Ready
Open source
https://www.kickstarter.com/projects/gfw/puckjs-the-ground-breaking-bluetooth-beacon
Basically a Compact, Cooler-looking Arduino Board + Sensors

## Slide 8: Open Source
Hardware, Software, libraries and documentation are all Open Source
  Can replicate the design
  Use cheaper hardware/manufacturers
Everyone can contribute
  Report bugs and issues on the official forums.
  The creator is very active in answering queries and suggest fixes for future patches
Weakness: Undocumented errors, Slow firmware update (dependent on one creator)
Notes: Pls fill in this page thank you very much

## Slide 9: Cost
https://www.digikey.com/product-detail/en/panasonic-bsg/CR2032/P189-ND/31939
USD
Puck.js: 39.95 USD
Battery
CR2032 (225mAh) (20mm)
Battery life:
Best Case
11250 hours = 1.3 years
(Basic advertising only, does not use sensors or LED)

## Slide 10: Cost – Other IoT beacons
Components could be bought cheaply if we are manufacturing in-house
Nordic nRF52832 module: US$0.1-0.2 (Alibaba)
  http://www.alibaba.com/product-detail/Module-Bluetooth-4-2-NORDIC-NRF52832_60594820230.html?spm=a2700.7724838.0.0.Gfk9YD
Nordic nRF52832 beacon: US$1-10 (Alibaba)
  https://www.alibaba.com/product-detail/Motion-sensor-nRF52832-beacon-ble_60410946591.html?spm=a2700.7724838.0.0.Gfk9YD&s=p

## Slide 11: Sensors
MAG3110 Magnetometer
Infrared Transmitter
Thermometer
Light sensor
Battery level sensor
Capacitive sensing pin
NFC tag

## Slide 12
2. Begin programming!
1. Download Web IDE (Windows)
Chrome (Android)
How It Works

## Slide 13
No programming knowledge required – Graphic IDE Included
But basic knowledge in JavaScript recommended
Requires Bluetooth connection on the programming device
Windows – Install Web IDE
Android - Android 6 (Marshmallow) or later required
  Android 5 works with latest Chromium build
Mac OS - OS X Yosemite above
Chromebook – all supported
Linux - BlueZ 5.41+ required
Requirements

## Slide 14
Originally used as compass
Can be configured to use as a metal detector
Example: Use magnetometer to detect presence of car in parking lot
Overview - Magnetometer
Notes: +how the sensors work, no need emphasize the use cases

## Slide 15
Device which measures magnetic fields
Senses magnetic flux density  detects fluctuations in the Earth’s field
Vector magnetometer: measure flux density value in 3 dimensional space
Common application: compass, location tracking
Overview - Magnetometer
Notes: +how the sensors work, no need emphasize the use cases

## Slide 16
Puck.mag() function returns the magnetometer reading in three dimensions (x, y, z)
Use root mean square function (RMS) to convert the reading into a more manageable form
Weakness: Moving the magnetometer will affect reading
Overview - Magnetometer
Notes: +how the sensors work, no need emphasize the use cases

## Slide 17
How it works: The capacitive sensor sense the change in capacitance in the surrounding area of the antenna, which is affected by the dielectric of the object nearby. (e.g. Dielectric of air < Dielectric of water)
Puck.js contains a capacitive sensing pin (D11).
Attach the pin to a large surface area using wire to increase sensitivity of sensing capacitance change.
Overview – Capacitive Sensor
Notes: +how the sensors work, no need emphasize the use cases

## Slide 18
Able to sense the presence of liquid – use as water level sensor
Can tell difference between different water levels
Overview – Capacitive Sensor

## Slide 19
Able to sense the presence of solid – use as gun detector
Can tell difference between empty and full gun holster
Overview – Capacitive Sensor

## Slide 20
Puck.capSense() returns the capacitive sensor reading as an integer
Code below prints out the capacitive sensor reading every 1000ms/1s
Weakness: Needs an external antenna to extend the range, else it only uses the original pin which has extremely short range (<5mm)
Overview – Capacitive Sensor
Notes: +how the sensors work, no need emphasize the use cases

## Slide 21
Broadcast message using Bluetooth
Supports multiple formats e.g. Eddystone, iBeacon
Overview – Bluetooth Beacon
On PC
Google Beacon Tools app on Android

## Slide 22
Broadcast message can be defined by user
  URL
  Battery Level
  Sensor reading
  etc.
Transmission power and rate can be configured
Maximum range: ~50m
Overview – Bluetooth Beacon

## Slide 23
Open BLE beacon format from Google
Part of Google beacon platform
Can be detected by both Android and iOS devices
Can broadcast different types of payload:
  Eddystone-UID: unique and static ID
  Eddystone-URL: compressed URL
  Eddystone-TLM (telemetry): beacon status data, should be interleaved with UID/EID, encrypted eTLM version is available
  Eddystone-EID: time-varying beacon frame, resolved to stable information by a linked resolver, such as Google Proximity Beacon API.
Puck supports Eddystone-URL
Overview – Eddystone

## Slide 24
Simple way:
  require(“ble_eddystone”).advertise(“goo.gl/B3J0Oc”);
Another way:
  NRF.setAdvertising(<data>, <options>)
  Allows you to customize the data to be sent through Bluetooth
Overview – Bluetooth Beacon
https://www.espruino.com/Reference#l_NRF_setAdvertising
NRF.setTxPower()
Configure the transmission power (in units of dBm)
Notes: +how the sensors work, no need emphasize the use cases

## Slide 25
There are two types of Bluetooth broadcast that is supported by the Puck.js
Advertising
  The Puck advertise a Bluetooth message, it might or might not have a receiver
  Message can be read by all other beacons/Bluetooth scanners nearby
  e.g. BLE Mesh
Pairing
  The Puck searches for a receiver, establish a connection with it, then transmit the message
  Can tell when the message is transmitted and received successfully (Using UART over BLE)
  e.g. Puck to Puck communication
Overview – Broadcasting
Notes: +how the sensors work, no need emphasize the use cases

## Slide 26
Puck can listen to other Bluetooth broadcasts nearby
Can act as a relay to increase the effective range of broadcast
Puck to Puck communication has been tested
Maximum range: ~10m (unobstructed)
Overview – BLE Mesh
Use case:
Puck broadcast sensor data
Sensor data read by nearby Pucks and rebroadcasted
Extend range + Ensure data gets to the intended recipient (e.g. a gateway)

## Slide 27
Connection between three IoT controllers possible
Able to expand to much more IoT controllers in the future
Overview – Bluetooth Mesh
Notes: +how the sensors work, no need emphasize the use cases

## Slide 28
Puck #1 broadcast temperature data (using NRF.setAdvertising())
Puck #2 will scan for Bluetooth broadcast from Puck #1. If found, it will rebroadcast the same temperature data
When the micro:bit detects the temperature data, the LED on board will turn on.
Note: only Puck #1 and #2 requires programming beforehand, the micro:bit does not contain any preloaded code
Overview – Bluetooth Mesh
Puck #1
Puck #2
Micro:bit
Notes: +how the sensors work, no need emphasize the use cases

## Slide 29
The sender Puck can scan all nearby Bluetooth devices and filter out the devices you want to connect to.
No prior configuration on the receiving Puck is required
But if specific user defined functions is required, need to define on receiving Puck first
  E.g. the rebroadcast() function in the picture below
Overview – Puck to Puck Comm.
Notes: +how the sensors work, no need emphasize the use cases

## Slide 30
Light Sensor
  Measure the “brightness” of the environment around the Puck
Temperature Sensor
  Measure surrounding temperature
NFC (Near Field Communication)
  Broadcast any data, can be received by NFC-enabled phones
IR (Infrared)
  Act as a controller, can be used as a power on switch
GPIO Pins, LED and Button
  GPIO Pins capable of PWM, SPI, I2C, UART, Analog Input
  Three LEDs for indication or alert purposes
  Push button can be used for user input
Overview – Other Features

## Slide 31
Update using nRF Toolbox App (Android & iOS)
Download the binaries from the official site
Reset the Puck and boot it in debug mode
Upload the firmware to the Puck using the app
Puck.js is still actively developed – firmware updates to provide new functions are released occasionally
Potential BLE5-supporting firmware
Overview – Update Firmware

## Slide 32
Materials:
  Tablet with Web Bluetooth enabled/PC
  Puck.js
Steps (For Tablet):
  Open Chrome Web Browser on the tablet
  Navigate to http://www.espruino.com/ide/
  Connect to the Puck by clicking the top left button (Yellow)
Hands on (1)
PC

## Slide 33
For Windows user
Steps (For PC):
  For PC, go to goo.gl/uK7Fz1 and install the Web IDE
  Connect the Puck to your PC (Through Bluetooth options)
  Connect to the Puck by clicking the top left button in the IDE (Yellow)
Hands on (PC-1)

## Slide 34
Hands on (2)
Steps:
  4. Click the “Upload code” button
  5. The red LED on the Puck should be blinking now

## Slide 35
There are several codes preloaded in the tablet to showcase the sensors
Feel free to try them out!
Hands on (3)
Training Codes:
goo.gl/YG165W

## Slide 36
Training_LED.js
Use the button to turn the LED on and off
Training_Magnetometer.js
Turn on Green LED when metal is close by (e.g. scissors/some smartphones)
Training_capSense.js
Turn on Red LED when a finger is placed on D11
Training_Puck2Puck_Master.js
Training_Puck2Puck_Slave.js
The Master Puck can control the Slave’s LED
Hands on (4)
Training Codes:
goo.gl/YG165W
Notes: Bluetooth mesh, puck to puck, tx power, rate, firmware update

## Slide 37
Training_Light.js
Turn on the LED when dark (cover the Puck with your fingers)
Other individual instructions
digitalWrite(LED1, 0) – LED1/2/3, 0/1
E.getTemperature – get temperature in C
Puck.getBatteryPercentage()
Puck.light() – light sensor
Puck.mag() – get magnetometer reading (x,y,z coordinates)
Hands on (5)
Training Codes:
goo.gl/YG165W

## Slide 38
What does this code do?
Setup
Download Exercise.js from the site above, fill in the blanks.
Press the button.
What does this function do?
Exercise
Training Codes:
goo.gl/YG165W

## Slide 39
Some considerations:
  Inconspicuous / size
  Range
  Bluetooth Mesh support
  Battery Life
Open source hardware design means we can replicate the design and manufacture ourselves to reduce cost
Other Bluetooth beacons can be used as substitute
More testing required
Conclusion

## Slide 40: Thank You

## Slide 41
IoT_Innovation – Puck.js – Part 1.pptx (Lee Han Cheng)
IoT_Innovation – Puck.js – Part 2.pptx (Dinh)
[PPT] NEA Gravitrap Water Level Sensing Project.pptx (Ting Yi)
https://www.espruino.com/Puck.js
References